PRELIMINARY DESIGN REPORT

1. MIPS Program with the Given Subprograms

## Program for Part 1 of Lab 2
## Converts hexadecimal string to decimal number
## Mert Alp Taytak

.text
.globl __start

__start:

jal interactWithUser

# Print decimal value
move $t0, $v0 # $v0 will change for syscalls
la $a0, str3
li $v0, 4
syscall

# $t0 is the value
move $a0, $t0
li $v0, 1
syscall

li $v0, 10
syscall

# Before call: $a0 is the address of the string
# After call: $v0 is the decimal and non-string representation of the string
convertHexToDec:

# $a0 has the string address
# Save return address to stack and get string length
addi $sp, $sp, -20
sw $s2, 16($sp)	# It will be modified to hold current character
sw $s1, 12($sp)	# It will be modified to hold current index in string
sw $s0, 8($sp)	# It will be modified to hold decimal value
sw $a0, 4($sp)	# It will be modified in strLength
sw $ra, 0($sp)	# Save return address for the caller

jal strLength

# $v0 is now string length
move $s1, $v0

# Restore $ra and $a0 from stack
lw $ra, 0($sp)
lw $a0, 4($sp)
addi $sp, $sp, 8

# Now: $a0 is string address, $s1 is string length
li $s0, 0	# Use $s0 for decimal value
sub $s1, $s1, 1 # Index starts from length - 1
# Use $s2 as current character

loopConvertHexToDec:
blt $s1, $zero, isValid # End of loop

lb $s2, 0($a0) # Load current character

blt $s2, 48, isInvalid	# Character is not a hexadecimal value
blt $s2, 58, isBetween_09	# Character is between 0 and 9
blt $s2, 65, isInvalid	# Character is not a hexadecimal value
blt $s2, 71, isBetween_AF	# Character is between A and F
blt $s2, 97, isInvalid	# Character is not a hexadecimal value
blt $s2, 103, isBetween_af	# Character is between a and f
j isInvalid	# Character is not a hexadecimal value

# In the following cases,
# the general idea is to get the true value of the character
# by subtracting some value corresponding to its ASCII value
# then using bitshift to get its decimal value corresponding
# to its place in the hexadecimal number and adding it to
# $s0 since it is keeping the final decimal value

isBetween_09:	# ASCII values 48-57
sub $s2, $s2, 48	# Value is now between 0 and 9
j shiftAndAdd

isBetween_AF:	# ASCII values 65-70
sub $s2, $s2, 55	# Value is now between 10 and 15
j shiftAndAdd

isBetween_af:	# ASCII values 97-102
sub $s2, $s2, 87	# Value is now between 10 and 15
j shiftAndAdd

shiftAndAdd:
sll $s0, $s0, 4	# Multilpy $s0 by 16 per hexadecimal digit for base conversion
add $s0, $s0, $s2	# Decimal value so far
sub $s1, $s1, 1	# Decrement index
add $a0, $a0, 1	# Increment address to next character
j loopConvertHexToDec	# Next iteration of the loop

isInvalid:	# Exit with error output
li $v0, -1	# Defined invalid input value
j exitConvertHexToDec	# Go to exit

isValid:	# Exit with converted value
move $v0, $s0	# Move decimal value to return register $v0
j exitConvertHexToDec	# Go to exit

exitConvertHexToDec:	# Restore $s registers from stack and return to caller

lw $s2, 8($sp)	# Restore old $s2
lw $s1, 4($sp)	# Restore old $s1
lw $s0, 0($sp)	# Restore old $s0
addi $sp, $sp, 12	# Reset stack pointer
jr $ra	# Return to caller

# Before call: $a0 is the address of the string
# After call: $v0 is the length of the string
strLength:

# $a0 has the string address

# $v0 will be the length counter
li $v0, 0

loopStrLength:
lbu $t0, 0($a0)	# Get next character
beqz $t0, exitStrLength	# If the character is null terminating character then exit the loop
beq $t0, 10, exitStrLength	# If the character is equal to new line then exit the loop
add $a0, $a0, 1	# Move to next character
add $v0, $v0, 1	# Increment length counter
j loopStrLength	# Loop again

exitStrLength:
jr $ra	# Return to caller with string length in $v0

# Before call: Takes no parameters
# After call: Returns no value
interactWithUser:

# Welcome user
la $a0, str0
li $v0, 4
syscall

interactMainBody:
# Ask and get string
la $a0, str1
li $v0, 4
syscall

la $a0, hex # Address of input buffer
la $a1, 10 # Maximum number of input characters, 32 bit = 8 hexadecimal with 1 null terminating character
li $v0, 8
syscall

# Save return address to the stack
addi $sp, $sp, -4
sw $ra, 0($sp)

# Call convertHexToDec
# $a0 should be address of the hexadecimal string
# $v0 will be the decimal value
la $a0, hex
jal convertHexToDec

# Restore return address from the stack
lw $ra, 0($sp)
addi $sp, $sp, 4

# If $v0 = -1 then input string was invalid
beq $v0, -1, invalidString

# Return to caller
jr $ra

invalidString:
la $a0, str2
li $v0, 4
syscall
j interactMainBody

.data
dec:	.word 0	# Initialize with 0
str0:	.asciiz "This program converts input hexadecimal string to its decimal equivalent number.\n"
str1:	.asciiz "Please enter your hexadecimal number (no more than 8 characters): "
str2:	.asciiz "Invalid hexadecimal number. Please try again.\n"
str3:	.asciiz "Your number in decimal: "
hex:	.space 10	# 8 hexadecimal digits and 1 null terminating character

2. Generation of the Machine Instructions

...
previous:	nop	# Address: 10 01 00 1C16 (as given)
nop	# Address: 10 01 00 2016
nop	# Address: 10 01 00 2416
nop	# Address: 10 01 00 2816
j	next	# Address: 10 01 00 2C16
nop	# Address: 10 01 00 3016
add	$t0 ,$t1, $t2	# Address: 10 01 00 3416
next:	j	previous	# Address: 10 01 00 3816

  J-TYPE = (OPCODE-6 bits) + (TARGET ADDRESS-26 bits)
 j next = (00 0010) (0000 0000 0001 0000 0000 0011 10)2 = 0800400E16
 j previous = (00 0010) (0000 0000 0001 0000 0000 0001 11)2 = 0800400716